## Slide 1: OIL SPILL DETECTION EMPLOYING SAR DATA AND MACHINE LEARNING
GROUP 8:
Abdul-raheem Umar
Kaushal Kishor
Patrícia C. Genovez
Rezaul Bhuiyan
FACULTY OF GEO-INFORMATION SCIENCE AND EARTH OBSERVATION - UNIVERSITY OF TWENTE
10 November 2023

## Slide 2: Agenda
Introduction
Data Set
Methodology
EDA
ML: Random Forest
DL: DeepLabV3+
DL: U-Net
Conclusion

## Slide 3: INTRODUCTION AND BACKGROUND
Monitor Remote Oceanic regions with difficult access
Wide Swaths: Covering Large Areas
Active Sensor: Day and Night Acquisition
Operate in all Weather Conditions
Near Real Time (NRT) Delivery
Oil Spills = Dark Spots
Main Limitation: False Alarms
Notes: Oil spills are unpredictable events that can occur anywhere at anytime
On the sea surface oils slicks rapidly spreads covering large areas
Depending on the wind and oceanic currents slicks can drift and reach coastal ecosystems
Causing different environmental and socio-economic impacts
For an effective oil spill response, a NEAR REAL TIME DATA PROCESSING IS NEEDED TO PROVID USEFUL INFORMATION FOR THE DECISION MAKERS
It is possible detect oils spills in different spectral ranges, optical, thermal, NIR, UV …. However Synthetic Aperture Radars area the most operational data providers
Allowing to monitor Remote offshore areas with difficult access
Covering large areas
During the day and the night
Operating in all weather conditions
Delivering data in near real time
IN SAR DATA OIL SPILS ARE DETECTED AS DARKS SPOTS DUE TO THE SPECULAR REFLECTION
Main limitation is that other phenomena are also BE detected as dark spots - generating false alarms

## Slide 4: WHY MACHINE LEARNING & DEEP LEARNING?
SAR Data Complexity: Speckle Noise (Multiplicative Noise), Background Noise, Different Statistical Distributions - Non-linear (Data Format)
Scale and Shape: Different Dimensions and Geometries depending on the type, the volume and the source of the oil slicks
Classes Ambiguity: other meteo-oceanographic events can also be detected as Dark Spots = False Alarms
SAR Scene Complexity: simple scenarios = well-defined and easy detectable Oil Spills, as well as complex scenarios with multiple dark spots.
Big SAR Data: Humanly Unfeasible process and interpret huge amount of data operationally.
Oil Spill Detection and Discrimination is Challenging:
Notes: SAR Data is Complex: Speckle Noise (Multiplicative Noise), Noise Equivalent Sigma Zero Noise (NESZ), Different Statistical Distributions - non-linear (Complex: MCG; Intensity: Exponential; Amplitude: Rayleigh)
Shape and Scalability: Different dimensions and geometries depending on the type, the volume and the source of the oil slicks, as well as on the wind and currents
Classes Ambiguity: other different meteo-oceanographic events are also detected as dark spots and generate false alarms
SAR Scene Complexity: simple scenarios with well-defined and easy detectable dark spots, as well as complex scenarios with multiple dark spots and meteo-oceanographic conditions.
Big SAR Data: Unfeasible for human processing and interpretation (Subjective: depends on the background of the interpreter)

## Slide 5: DATA AVAILABILITY AND POTENTIAL CHALLENGES
Krestenitis, M., Orfanidis, G., Ioannidis, K., Avgerinakis, K., Vrochidis, S., & Kompatsiaris, I. (2019). Oil spill identification from satellite imagedeep neural networks. Remote Sensing, 11(15), 1762.
Krestenitis, M., Orfanidis, G., Ioannidis, K., Avgerinakis, K., Vrochidis, S., & Kompatsiaris, I. (2019). Early Identification of Oil Spills inSatellite Images Using Deep CNNs. In International Conference on Multimedia Modeling (pp. 424-435). Springer, Cham.
Challenges: Classes Imbalance, Ambiguities, Adjust Codes to the Dataset, Hyperparameter Tuning
Benchmark: Oil Spill Detection Dataset
Number of Samples and Classes:
1,112 samples
5 classes:
0. Sea Surface
1. Oil Spill
2. Look-alike
3. Ship
4. Land
650
Image Size = 1250
Synthetic Aperture Radar
Ground Truth Mask
Objective: Train, Test, and Validate ML models to discriminate Oil Spills from Look-Alikes using SAR data.
Sentinel-1: Polarization - VV; Spatial Resolution - 10 m; Speckle Reduction - Median Filter 7x7
SAR image subsets: 1250 x 650 pixels
Ground Truth: Labels
OSD Dataset:

## Slide 6: METHODOLOGIES: TRADITIONAL ML AND DL
GLCM-contrast
Erosion
(Kernel)Filtering
Class Balancing
320x320

## Slide 7: Exploratory Data Analysis

## Slide 8: RANDOM FOREST MODEL IMPLEMENTATION

## Slide 9: RANDOM FOREST MODEL IMPLEMENTATION
Dataset (1112):
Training: 900
Validation: 200
Test: 100
Hyperparameters:
Number of trees:200
Max depth: 5

## Slide 10: RANDOM FOREST MODEL RESULTS
Sampling | VV + Texture | VV + Texture + Filters
Down | 0.40 | 0.42
Up | 0.40 | 0.41
Balanced | 0.868(0.13) | 0.877(0.15)
Overall Accuracy
Classification Report: Balanced model
Class | Precision |  | Recall |  | F1-Score |  | Support | 
Sea | 0.92 | 0.94 | 0.94 | 0.94 | 0.93 | 0.94 | 9337961 | 9337961
Oil | 0.32 | 0.37 | 0.38 | 0.47 | 0.34 | 0.42 | 816494 | 816494
Look | 0.22 | 0.32 | 0.00 | 0.19 | 0.00 | 0.23 | 154361 | 154361
Ship | 0.04 | 0.02 | 0.00 | 0.00 | 0.00 | 0.00 | 96344 | 96344
Land | 0.00 | 0.02 | 0.00 | 0.00 | 0.00 | 0.00 | 39640. | 39640
Original label
VV + Texture
VV + Texture + Filters
*IOU​

## Slide 11: DEEPLABV3+: IMPLEMENTATION
Parameters:
Epochs = 100
Activation Function = ReLU
Batch Normalization
Loss Function = Cross-entropy
Optimizer = Adam
Learning Rate = 5 x 10-5
Same Configuration used in the Dataset’ Paper:
Training: 1002
Test: 110
Classification Assessment:
Overall Accuracy
Loss Curve
Error Rate Curve
Intersection over Union (IoU)
DeepLabV3+ model Architecture for Semantic Segmentation
Batch Size = 12 Patch Size = 320

## Slide 12: DEEPLAB: RESULTS
Ocean
Oil
Lookalike
Land
Ship
Ocean
Oil
Lookalike
Land
Ship
Ground Truth Mask
Classification Map
SAR Data
Lookalike
Lookalike
Oil
Oil
Oil
Oil
Oil
Oil
Land
Lookalike
Lookalike
Lookalike
Oil
Oil
Oil
The thinner
Oil Slick
Not Detected
Dark Spots not
Mapped in
the Mask But Detected by the Semantic Segmentation
Confusion
Ocean
Oil
Lookalike
Land
Ship
Ocean
Oil
Lookalike
Land
Ship
Ground Truth Mask
Classification Map
SAR Data
Oil
Oil
Oil
Oil
Land
Oil
Oil
Oil
Oil
Lookalike
Lookalike
Oil
ok
Confusion
Confusion
Processing Time: 4hours
Classification Assessment:
Overall Accuracy: 96.47%
Loss : 0.0988
Intersection over Union (IoU): 0.4
Low Mean IoU indicates that the performance for the minor classes like oil spill and lookalikes were worst.
Converges
TR & TS = tendency
Trained Model matches to the TS
TR & TS = tendency
Trained Model matches to the TS
Class Imbalance

## Slide 13: UNET: IMPLEMENTATION

## Slide 14: UNET: RESULTS

## Slide 15: CONCLUSION: PERFORMANCE OF ML & DL
TRADITIONAL ML
RF
Original Data:
Overall Accuracy: 87%
Mean IOU: 0.1
HANDCRAFTED FEATURES: EDA
KNOWLEDGE DRIVEN: Background and experience of the interpreter
FEATURES = FLATTENED VECTOR: Spatial context is lost
DEEP LEARNING
Deep
Lab
Overall Accuracy: 96.47%
Loss : 0.098
Mean IoU: 0.4
UNet
Overall Accuracy: 88.00%
Loss : 0.89
Mean IoU: 0.5
FEATURE MAPS: Automatic learned through the Convolutional Layers
DATA DRIVEN: Less subjective can handle SAR data automatically
FEATURES = IMAGES: Spatial context is preserved
CONVOLUTIONAL LAYERS: Features in different levels of abstractions  Local and Global Context of the targets improving the Semantic Segmentation (Pixel Wise Classification)
DL Handle: Dark Spots Ambiguity and Capture Different Shapes and Dimensions

## Slide 16: THANKS FOR YOUR ATTENTION